Data Link Layer

- Layer 2 in the OSI Reference Model

- Translates and passes data between Physical Layer and Network Layer

- Ethernet operates at this level

- Has two sublayers, based on functionality

  - Logical Link Control (LLC)

  - Media Access Control (MAC)

Logical Link Control (LLC) Sublayer

- IEEE 802.2

- Interfaces with Network Layer protocols (e.g., IPv4, IPv6, ICMP)

- Translates IP packet into a frame

- Performs error checking and control—requests retransmission of frames that fail error checking

  - Error checking is performed by destination node

  - Frame is discarded and retransmitted

- Manages flow control between nodes

- NOTE: Flow control and error checking is also performed by Transport Layer protocols (e.g., TCP/IP)

Media Access Control (MAC) Sublayer

- IEEE 802.3

- Interfaces with physical media and controls access, such as through CSMA/CD

- Every network-enabled device has a network interface controller (NIC)

- Every NIC has a 48-bit unique address, called a MAC address

  - Displayed as 12 hexadecimal digits (00:00:00:00:00:00)

  - First 6 are vendor code specified by IEEE

  - Last 6 are assigned by manufacturer and are unique to that vendor

- Some devices allow the user to change the MAC address

Discussion Topics:

- Do you see any benefit to making LLC and MAC their own layers instead of sublayers?

- What are the pros and cons of allowing users to change MAC addresses? Could this be used as a form of network attack?

- Why is flow control an important service of LLC?