Alignment of Ethernet Networking Components to Transmission Rate

| Ethernet Networking Component | Transmission Rate (in MBits/s) |
| --- | --- |
| Category | Component |  |
| Cabling | Thick Coaxial | 10 |
|  | Thin Coaxial | 10 |
|  | Category 3 Twisted Pair | 10 |
|  | Category 5 Twisted Pair | 10/100 |
|  | Category 5e Twisted Pair | 10/100/1000 |
|  | Category 6 Twisted Pair | 10/100/1000/10000 |
|  | Fiber Optic | 10/100/1000/10000 |
|  | Twinaxial | 10000 |
|  | Copper Printed Circuit Board | 1000/10000 |
| Network Interface Cards | PCI/PCI Express Adapter Card | 10/100/1000 1000/10000 |
|  | USB Network Adapter | 10/100/1000 |
| Connection Points | Hub | 10/100 |
|  | Switch | 10/100/1000/10000 |
|  | Router | 10/100/1000/10000 |

Remember:

- Cabling within a particular type (e.g., twisted pair) is generally backwards compatible

- Low-speed networking components are still available and are still in use due

  - Low cost

  - Legacy systems not supporting higher transmission rates