IPv4 Background

- Fourth version of IP addressing scheme

- RFC 791 standard published in 1981 by Internet Engineering Task Force (IETF)

- 32 bit address length = 232 addresses

- In the 1990s, it became apparent there would soon be a shortage of IP addresses

- IPv4 unable to keep up with rapid growth of networked hosts and network-ready devices

- Primary address pool of IPv4 addresses was exhausted on February 3, 2011

Introducing IPv6

- Sixth version of IP addressing scheme

- RFC 2460 published in 1998

- 128 bit address length = 2128 addresses

- Significant structural differences from IPv4 (see table below)

- Currently in a transition phase – operating systems have a dual IP stack in order to support both IPv4 and IPv6

- IPv6 provides support for IPv4 addresses

Comparison of IPv4 and IPv6

|  | IPv4 | IPv6 | Improvement |
| --- | --- | --- | --- |
| Address Length | 32 bits | 128 bits | Significantly more addresses available |
| # of Addresses | 232 | 2128 |  |
| Syntax | 192.168.0.1 | 2002:0:0:0:0:0:a80c:502b | Clear separation of network (first 64 bits) and host (last 64 bits) identification. Long address can be compressed |
| Network Prefix | Variable | Fixed 64 bits | Improves routing speed |
| Host Identifier | Manual or DHCP | Automatic | Eliminates possibility of IP address conflict Reduces administrative overhead |
| Methodologies | Unicast Broadcast | Unicast Anycast Multicast | In IPv4, multicast was supported only through a reserved address class; in IPv6, multicasting is native IPv6 introduces anycasting, in which a packet is sent to the closest host in a specified host group IPv6 disposes of broadcasting, reducing network congestion, and eliminating an attack vector |