## Slide 1
IS3120 Network Communications Infrastructure
Unit 6
Layer 2 Networking, VLANs,
and Resiliency

## Slide 2: Learning Objective
Design a Layer 2 network with VLANs and resiliency.

## Slide 3: Key Concepts
Layer 2 networking features and capabilities
Virtual LANs
Layer 2 network resiliency
Layer 2 network design
  Workgroup LAN
  Departmental LAN
  Layer 2 network trunking
  Building collapsed backbones

## Slide 4: EXPLORE: CONCEPTS

## Slide 5: Layer 2 Concepts
Defines the physical addressing of network nodes and provides the means for a LAN to deal with media transmission issues
Protocols control access to a shared medium (copper, fiber, radio waves)
Used everywhere
  From end-point, desktop/workstation connectivity to WAN connections
Notes: Layer 2 refers to the Data Link Layer in the Open Systems Interconnection (OSI) Reference Model.

## Slide 6: Layer 2 Features and Capabilities
Hardware-based bridging (MAC)
Low latency
Low cost
Power over Ethernet (PoE)
High speed; 100/1000/10000 Ethernet LAN connectivity

## Slide 7: VLANs
A collection of nodes grouped together in a broadcast domain that’s based on something other than physical location
Splitting switches into separate virtual switches
VLAN
Notes: Provide segmentation based on LAN broadcast domains
Allow you to split switches into separate (virtual) switches
 Only members of a VLAN can see that VLAN’s traffic
 Inter-VLAN traffic must go through a router
VLANs address scalability, security, and network management
Trunking from wiring closet to building or campus backbone

## Slide 8: Link Aggregation/Trunking
Also known as port bundling, link bundling
Uses multiple links in parallel as a single, logical link
  Increases capacity
  Is redundant (fault tolerant)
IEEE 802.3ad
Link Aggregation Control Protocol (LACP)
Notes: LACP is a standardized method of negotiating bundled links between switches.
LACP operation:
Two switches connected via multiple links will send LACPDU packets, identifying themselves and the port capabilities
They will then automatically build the logical aggregated links, and then pass traffic.
Switch ports can be configured as active or passive
Background resources: http://www.cisco.com/en/US/docs/ios/12_2sb/feature/guide/gigeth.html and IEEE Standard 802.3ad, Link Aggregation.

## Slide 9: Network Resiliency
High availability
Redundant paths
Failure resistance
Notes: Network Resiliency
Is the ability of the network to:
-Respond to failure
-Resist failure
-Handle demand fluctuations with little or no impact on service delivery
Includes redundant, multiple paths; avoids a single point of failure (SPOF)
Offers high availability
Scope of resilient network infrastructure includes:
Hardware – servers, storage, controllers, workstations, laptops, mobile devices,
Software/applications
Building wiring infrastructure
Networking devices -- hubs, routers, switches
Voice and voice equipment
Management software and services

## Slide 10: EXPLORE: PROCESSES

## Slide 11: Design a Layer 2 Network
Star topology
Hierarchical
Modular
Switched; one switch as aggregation (or backbone)
Notes: Always connect hierarchically
 If a building has multiple switches, use an aggregation switch
 Locate the aggregation switch close to the building entry point, for example, the fiber panel
 Locate edge switches close to users, such as one per floor
 Remember: The maximum length for Cat 5 is 100 meters
Minimize paths between elements
Build incrementally
Connect building hierarchically

## Slide 12: Design a Layer 2 Network
Core (backbone)
  Resilient, few changes, few features, high bandwidth, CPU power
Distribution
  Aggregation, redundancy
Access
  Port density, affordability, security features, many adds, moves, and changes
Notes: Core
- The backbone of a network
Includes high-end switches and high-speed cables such as fiber
Does not route traffic at the LAN
Deals with speed and ensures reliable delivery of packets
Distribution
Includes LAN-based routers and Layer 3 switches
Ensures packets are routed properly between subnets and VLANs in the enterprise
Access
Includes hubs and switches
Focuses on client node connections (e.g., workstations to the network)
Ensures packet delivery to end-user computers

## Slide 13: Core, Distribution, Access
Backbone
CORE
ACCESS
DISTRIBUTION
Notes: 1. Determine number of VLANs required
One per department?
2. Determine VLAN parameters
3. Determine VLAN port assignments
4. Configure VLANs
-Determine switch configuration switch with ports on the appropriate VLAN
-Assign an IP address that belongs to the proper subnet
-Determine correct port on switch for host
-Assign correct IP address to host depending on VLAN membership

## Slide 14: Design a VLAN
Number of VLANs
Parameters
ID, Name, Media Type, more
Port assignments
Access port
One per department
Trunk port
Notes: 1. Determine number of VLANs required
One per department?
2. Determine VLAN parameters
3. Determine VLAN port assignments
4. Configure VLANs
-Determine switch configuration switch with ports on the appropriate VLAN
-Assign an IP address that belongs to the proper subnet
-Determine correct port on switch for host
-Assign correct IP address to host depending on VLAN membership

## Slide 15: EXPLORE: ROLES

## Slide 16: Layer 2 Network Roles
Workgroup LAN
Departmental LAN
VLAN/Layer 2 network trunk
Building collapsed backbone
Notes: Workgroup LAN
Usually physically located in the same geographical area of a building
Connect groups of devices used by small groups of people who often share similar job functions
Is usually a subset of a much larger, functional department
Department LAN
Superset of the workgroup LAN
Connects workgroup LANs but keeps them separate: each workgroup LAN is a separate broadcast domain or collision domain
Departmental LANs needed when workgroups are physically located in different wiring closets
VLAN
- Group network devices that communicate with one another as if they were part of a single broadcast domain
- Creates multiple groups of associated network nodes without having to use Layer 3 routers
Layer 2 network tunneling
- Allows information from multiple VLANs to be carried over a single link between switches
Building collapsed backbone
Minimizes traffic flowing between departmental LANs given that they can transfer frames and packets at high speeds on a common backplane

## Slide 17: EXPLORE: CONTEXTS

## Slide 18: Layer 2 VLAN Trunking Design
Without VLANs
Sales
10.1.0.0/16
Marketing
10.2.0.0/16
Accounting
10.3.0.0/16
Notes: RFC 3069: VLAN Aggregation for Efficient IP Address Allocation
RFC 4554: Use of VLANs for IPv4-IPv6 Coexistence in Enterprise Networks

## Slide 19: Layer 2 VLAN Trunking Design
With VLANs
Sales VLAN
10.1.0.0/16
Marketing VLAN
10.2.0.0/16
Accounting VLAN
10.3.0.0/16

## Slide 20: EXPLORE: RATIONALE

## Slide 21: Cisco and HP Network Resiliency
Cisco
Multiple solutions
HP
Intelligent Resilient Framework (IRF)
Notes: Cisco and HP have different solutions
Cisco:
Resilient Ethernet Protocol (REP) - for Ring
Resilient Services Solution for Campus Networks (http://www.cisco.com/en/US/netsol/ns340/ns394/ns147/ns17/index.html)
Connected Grid (which combines Cisco 2010 Connected Grid Router and Cisco 2520 Connected Grid Switch)
HP Intelligent Resilient Framework (IRF)
Why the need for the HP solution? IRF is simpler to manage, boasts higher performance, more resilient, and has a flatter network design.

## Slide 22: IRF
IRF is an innovative HP switch platform virtualization technology that allows customers to dramatically simplify the design and operations of their data center and campus Ethernet networks.
http://h17007.www1.hp.com/us/en/networking/solutions/technology/irf/#.VxqdIq4o7IU

## Slide 23: Summary
In this presentation, the following were covered:
  Layer 2 networking features and capabilities
  Virtual LANs (VLANs)
  Layer 2 network resiliency
  Layer 2 network design
  VLAN trunking