## Slide 1: NT1110 Computer Structure and Logic
Unit 8 (Module 5A)
COMPUTER OPERATION AND SECURITY
Notes: 1

## Slide 2: Class Agenda 7/29/16
Chapter 7 and 9
Learning Objectives
Discussion on Assignments and Lab.
Break Times as per School Regulations.
Assignment will be given in the next class
Reading Assignment.

## Slide 3: Learning Objectives
To understnd
Basic Input/Output System (BIOS), Complementary Metal–Oxide–Semiconductor (CMOS), and Firmware
How to Configure the System BIOS
Power-On Self-Test (POST) and Error Reporting

## Slide 4: How Startup BIOS Controls the Boot Process
Startup BIOS on motherboard in control until operating system loaded and takes over
PC technician must understand how startup BIOS controls the boot
  Knowledge helps in troubleshooting a failed boot before operating system loaded

## Slide 5: Hardware Configuration (cont’d.)
CMOS RAM
  Also called clock/nonvolatile RAM (RTC/NVRAM)
  Retains data even when computer turned off
  BIOS settings are in motherboard manual
  CMOS battery enables CMOS RAM to hold configuration data

## Slide 6: Where Is BIOS Found?
  Firmware:
    Software that comes embedded in its own memory chip.
  Two types of memory used for BIOS firmware:
    EEPROM
      Electronically Erasable Programmable Read-Only Memory.
    EPROM
      Erasable Programmable Read-Only Memory.
      Older PCs used EPROM.
      Could be erased by exposure to ultraviolet light.
        Also known as “Flashing the BIOS.”
  Motherboard is set up to initialize its operations using BIOS.
Notes: EPROM was erased by exposure to ultraviolet light (hence the term flashing the BIOS)
EEPROM is Electronically erasable programmable read only memory, thus it can be updated. It is powered by a small battery

## Slide 7: BIOS Locations (Look for Battery)

## Slide 8: What Is CMOS?
CMOS = Complementary Metal Oxide Semiconductor
  A type of Random Access Memory (RAM).
  Memory can be lost without a power source.
  On-board battery keeps this functional.
CMOS stores settings used by BIOS:
  Boot sequence; hard drive parameters.
  BIOS/CMOS access password.
  These options are passed to the BIOS soon after the power is turned on.
  Settings can be changed by using the CMOS editor.

## Slide 9: The Startup BIOS Controls the Beginning of the Boot
Contained on motherboard firmware chip
Successful boot
  Hardware, BIOS, operating system all perform without errors (beeps, text or voice messages)
Boot functions
  Startup BIOS runs POST and assigns system resources
  Startup BIOS program searches for and loads an OS
  OS configures system and completes its own loading
  Application software is loaded and executed

## Slide 10: Step 1: Post and Assignment of System Resources
Turn on PC power
  Processor begins the boot by initializing itself
  Turns to startup BIOS for instructions
    Startup BIOS first performs POST
    17 key steps involved

## Slide 11: Step 2: Startup Bios Finds and Loads the OS
Startup BIOS looks to CMOS RAM to find boot device
Figure 5-35 For a successful boot, a hard drive must contain a healthy Master Boot Record (MBR) and a healthy OS boot record
Courtesy: Course Technology/Cengage Learning

## Slide 12: Step 2: Startup Bios Finds and Loads the OS (cont’d.)
Tracks: concentric circles on drive
Sectors (segments): portion of a track
  Holds up to 512 bytes of data
Master Boot Record (MBR)
  Contains master boot program and partition table
OS boot record
  512-byte sector
  Second sector on drive behind MBR
  Contains small program pointing to a larger OS program file (BootMgr or Ntldr)

## Slide 13
Figure 5-36 Numbered steps show how BIOS searches for and begins to load an operating system (in this example, Windows Vista is the OS)
Courtesy: Course Technology/Cengage Learning

## Slide 14: Configuring the Motherboard Using BIOS Setup
Access BIOS setup program
  Setup screen appears with menus and Help features
  Change system features
Table 5-9 How to access BIOS setup

## Slide 15
Figure 5-59 BIOS Setup Main menu
Courtesy: Course Technology/Cengage Learning

## Slide 16: Sample CMOS Editor
Notes: Be very careful about allowing students to enter the CMOS setup utility screens. This is not to say that they should not; in fact, they should, but you want to make sure that they do not change things that they are not familiar with, which in this type of class, will be most everything. If you have access to an LCD projector, being able to show them how a change would be made can be very useful, while also removing the mystery of how to make such changes. In reality, there are very few changes that need to be made in most modern PCs. Being familiar with the BIOS settings in Table 4-3 will be a very good way to get past most A+ exam questions on BIOS settings.

## Slide 17: Configuring the Motherboard Using BIOS Setup (cont’d.)
Change boot menu in BIOS setup
  Set boot sequence
Startup password allows access to computer
  Enabled and set in BIOS setup
  Password stored in CMOS RAM
  Changed by accessing setup screen
Exit screen options
  Save or discard changes and exit program
  Restore default settings
  Save changes and remain in program

## Slide 18: Configuring the Motherboard Using BIOS Setup (cont’d.)
Brand-name computer manufacturers
  Use their own custom-designed setup screens
CMOS RAM setting is lost if battery goes bad or disconnected
  Restore default settings
  Restore customized settings from written record of all changes
    Important to keep records up to date, stored with the hardware documentation in a safe place, well labeled

## Slide 19: How to install Windows
Plan the installation.
Chose the windows operating system
There are more windows version
Check for the system requirement for the OS

## Slide 20: Choose the Method of Installation
Installation choices
  Boot media
  Network installation
  Hard drive image
  Recovery CDs and DVDS
  Factory recovery partitions
  Repairs to existing installation
  Virtual Machine.

## Slide 21: virtual computer
Installation in a virtual computer
Virtual computer or virtual machine
Software simulating hardware of a physical computer
Allows installation and running of multiple operating systems at the same time on a PC
Reason to use a virtual machine
Train users, run legacy software, and support multiple operating systems
Can capture screen shots of boot process in a virtual machine

## Slide 22: Choose the Type of Installation: Upgrade, Clean Install, or Dual Boot
Installing Windows on a new hard drive
  Perform a clean install
Windows already installed on hard drive
  Clean install
    Overwrite existing operating system and applications
  Upgrade (if allowed)
    Upgrade Windows 7 to 8
    Upgrade Windows 7 to Windows 10
  Dual boot
    Install Windows 7/Windows 8 in a second partition

## Slide 23: Performing a Clean Install or Dual Boot
Steps
  1. Boot directly from Windows Vista CD/DVD/USB or ISO image fro a virtual Machine.
    Click Install now
  2. Enter product key and accept license agreement
  3. Choose Custom (advanced) for type of installation
  4. List of partitions displayed
    Make selection and click Next
  5. Drive options (advanced)
    Click New, enter size of partition, click Apply
  Installation continues

## Slide 24: Performing a Clean Install or Dual Boot
Enter user name, password, computer name, date, time, update preference
User name is assigned administrative permissions
Setup checks computer performance
Logon screen appears

## Slide 25: What to Do After the Vista Installation
Verify network access
Activate Windows
Install Windows updates and service packs
Configure automatic updates
Configure Vista components
Install hardware
Install applications

## Slide 26: Hands On Activities.
Inspecting the BIOS
Installing Windows 7.

## Slide 27: Assignment and Lab
Short Answer: Answer questions on BIOS.
Lab: Complete the lab titled “Understanding BIOS and POST.”